## Slide 1
Allotrope Framework Drives Innovation In LabInformatics
Dr. Gerhard Noelken
Allotrope BoD member, Pfizer Allotrope Liaison
Chemical Information and Computer Applications, RSC London
20 October 2015

## Slide 2
2
MOTIVATION
THEORY
REDUCING IT TO PRACTICE

## Slide 3: Why is access to music so much easier than access to scientific data?
Think about scientific data...
Material
Equipment
Process
Result
.dat
.tbl
.HDF
.csv
.DAML
.LCD
.XML
.jdx
.irf
.pdid
.drdd
.asc
.cdf
.frx
.raw
Scientific data is typically stored in a wide variety of non-standard,
proprietary formats…
…with contextual metadata that are hard to find and sometimes inconsistent
...making it costly and sometimes difficult to find and get value from it.
Think about music...
Artist
Album
Song
Genre
Date
Artwork
Music is typically stored in a small number of standard, non-proprietary
formats…
…with contextual metadata that are complete, consistent & correct
…enabling the user to find, share and enjoy it years later from any device easily!

## Slide 4: What if scientific data was as easy to access as music?
  Store scientific and process data in a standard format with contextual metadata that is...
    correct
    complete
    consistent
    compliant
  Find data in seconds.
  Be confident that the data that underpins our decisions is accurate, complete, and compliant.
  Build data quality and data integrity into the system, eliminating the need for many SOPs and quality investigations.
  Simplify, automate and improve laboratory and manufacturing processes.
  Automatically create technical reports, audit trails, and substantial portions of regulatory submission documents.
  Answer complex questions, not just those accessible via simple queries - by linking data from diverse, disparate sources.
If we...
We could...

## Slide 5: Allotrope Foundation
Member Companies
Subject Matter Experts
Project Funding
Framework Development
Technical Leadership
Professional Software Firm
Secretariat
Project Management
Legal & Logistical Support
Partner Network
Requirements & Specifications
Contributions, PoC Applications
AbbVie
Amgen
Baxter
Bayer
Biogen
Boehringer Ingelheim
Bristol-Myers Squibb
Eli Lilly
Genentech/Roche
GlaxoSmithKline
Merck & Co.
Pfizer
ACD/Labs
Agilent
Biovia
BSSN
IDBS
Mestrelab Research
Mettler Toledo
Persistent
Riffyn
Sartorius
Shimadzu
Thermo Scientific
Waters
Erasmus Univ. Med Center
University of Southampton

## Slide 6
MOTIVATION
THEORY
REDUCING IT TO PRACTICE

## Slide 7: What is Allotrope Creating?
Allotrope Foundation Framework
Reusable Software Components
Standard File Format
Open Metadata Repository
Application 1
Application 2
Metadata repository
New Instrument
Instrument
.etc
.etc
.etc
.etc
.etc
.etc
.etc
.etc
.etc
.etc
.dat
.tbl
.HDF
.raw
.csv
.DAML
.LCD
.XML
.mzML
.jdx
.irf
.pdid
.drdd
.asc
.cdf
.frx
.adf
File format for any technique or instrument
Project | Test | Instrument
AF 0012354 | IR Fingerprinting | QC Lab #33B 380 FT-IR
AE0012764 | Bulk & Tapped Density | ASTM Standard Seive #6
AF 12989 | NMR Characterization | AM500
 | Tapped & Bulk Density | Sieve XXX
AF0045674 | Caractérisation RMN | Nouvelle DRX600
AF-0034558 | IR | iS10 FT-IR
Project | Test | Instrument
AF0012354 | IR Fingerprinting | 380 FTIR/-SN/145453
AF0012764 | Bulk and Tapped Density | ASTM Sieve-SN/3452
AF0012989 | NMR Characterization | AM500-SN/0034578
AF0013142 | Bulk and Tapped Density | ASTM Sieve-SN/09783
AF0045674 | NMR Characterization | DRX600-SN/10234567
AF0034558 | IR Fingerprinting | iS10 FTIR/-SN/341980
With the Metadata Repository
Standard vocabulary & structure for metadata
A toolkit that enables use of the standards & metadata in software development

## Slide 8: High Variability of Result Data
chromatography
pH
thermogravimetry
HPLC-MS-MS
…
mass spectroscopy
HPLC-MS
cell counter
NMR
Notes: NMR: nuclear magnetic repulsion spectrometry
We tackle the Variability Problem of BigData.

## Slide 9: Landscape of Existing Standards
ISO
W3C
IETF
OASIS
OMG
LC
CDISC
NISO
OAI
Notes: OAI: Open Archive Initiative
LC: Library of Congress
Evaluated: MZML, AniML, BatchML, ISA S88, …

## Slide 10: Key Requirements
Technical capabilities
Large data volume, small file size, fast
Platform independent
Comprehensive Metadata
Who, what, when, where, why and how
Long term data access
Documented file format
Vendor neutral format
Adaptable and extensible
Arbitrary techniques; extensible
Scientist, sample, time stamp/audit trail, instrument, purpose, method

## Slide 11: Allotrope Data Format (ADF)
* Use is optional
Data Description
RDF Model
Data Cubes
Universal data container
Data Package
Virtual file system *
Contains:
Method, instrument, sample, process, result, etc.
Data cube metadata
Data package metadata
…
Analytical data represented by one- or multidimensional arrays.
HDF5
Platform Independent File Format
Allotrope Data Format
Analytical data represented by arbitrary formats, incl. native instrument formats, images, pdf, video, etc.
Specifically designed to store and organize large amounts of numerical data.

## Slide 12: Allotrope Taxonomies: An Extensible Metadata Model
A library of extensible taxonomies
  Uses W3C standards
  Easy to understand and maintain by SMEs and Vendors
Start by harvesting existing available concepts
  PSI-MS; IUPAC; RSC Chemical Methods Ontology; Dictionary of weighing terms; AnIML, etc
  Reproducible & efficient collaboration model
  Leverages knowledge engineers & member company scientists
  2-3 weeks to develop initial version of a new taxonomy
Initial versions of 12 analytical techniques already implemented:
  gas chromatography
  Karl Fischer
  liquid chromatography
  mass spectrometry
  nuclear magnetic resonance spectroscopy
  thermogravimetric analysis
  ultra violet spectrometry
  cell counter
  cell culture analyzer
  blood gas analysis
  balance
  pH

## Slide 13: Allotrope Foundation Taxonomies
Notes: It quickly became clear that the Analytical Chemistry Domain needed a holistic approach to the taxonomies in order to cover the broad range of techniques, but also re-use lower level concepts- to get the right level of consistency and coherence
As opposed to technique-oriented approach
Thus the support of any particular technique in the ADF draws the appropriate terms and properties from the equipment, process and result domains

## Slide 14: The Big Picture
ADF Data Package
ADF Data Cube

## Slide 15
Result
Process
Equipment
Material
Common
Notes: The key to smarter data circular dendrimer – right now about 4K entities & properties. And is growing daily.

## Slide 16: ADF Class Library
  Platform independent file format
  (HDF 5)
Data Package API
Data Cube API
Data Description API
(Apache Jena)
Analytical Data API
Taxonomies
Triple Store API

## Slide 17: RDF Data Model
Subject-Predicate-Object (Triple)
Example: <Sample 1> type <Sample> <Sample 1> createdOn ‘2015-03-13’ <Sample 1> createdBy <person X> <Sample 1> hasBarcode ‘1234567890’
Subject
Predicate
Object

## Slide 18: Data Shapes Constrain How We Use Taxonomies in the Real World
  Taxonomies provide an unconstrained vocabulary that we can use to describe things (instances) in our open world and give them a meaning (= what it is)
  We need a mechanism to define data structures (schemas, templates) that describe how to use the taxonomies for a given purpose in a standardized (= reproducible, predictable, verifiable) way
  Shapes Constraint Language (SHACL, expressed as RDF triples) is an emerging standard to do this
http://www.w3.org/2014/data-shapes/charter

## Slide 19: Using Data Shapes: Equipment
Shape hierarchies define
additional constraints
A system has at least 1 component
A hplc system has at least 1 component and has at least 1 column, exactly 1 autosampler and at least 1 detector
A hplc-uv system has at least 1 component and has at least 1 column, exactly 1 autosampler and at least 1 detector
and at least 1 uv-detector

## Slide 20: The ADF enables a self-contained documentation of the data & metadata
Plan Analysis
Prepare Samples
Submit Samples
Control Inst. Acquire Data
Process Data
Analyze Data
Reports Results
Store, Archive Data
Request
Process
Step
Legend

## Slide 21: The ADF enables a self-contained documentation of the data & metadata
Plan Analysis
Prepare Samples
Submit Samples
Control Inst. Acquire Data
Process Data
Analyze Data
Reports Results
Store, Archive Data
Request
Data & Metadata
Process
Step
Legend
Standard data file format for data & metadata
Output from one system becomes the input to the next
The APIs enable the use of one vendor agnostic file format
Control Inst. Acquire Data
Process Data
Analyze Data
Interoperability
(Plug & Play)
Report & Share
Search & Reuse Data
More automated reporting,
Powerful searching
Analytical Method
Sample Prep Data
Instrument Instruction
Instrument Data
Processed Data
Analyzed Data
Reported Results
Stored Data

## Slide 22: Allotrope Data Format
Data Description
Data Cubes
Data Package(s) (optional)
Request
Sample prep
Method
Data acquisition
Instrument instruct.
Chromatogram 2D HDF
Chromatogram 2D HDF
Chromatogram: 3D HDF
Chromatogram: 2D HDF

## Slide 23
MOTIVATION
THEORY
REDUCING IT TO PRACTICE

## Slide 24: Reducing it to practice
Integration projects:
Early adoption and acceleration of AF Framework development through delivery of Framework components.
Accelerate vendor adoption via collaboration on delivering specific capabilities through the integration projects
Ensure the validity of the Framework through real-world requirements and implementation.
Benefit the sponsoring companies in terms of shared development of new functionality & shared experience
Drive integration of the Framework into the IT/IS Roadmap

## Slide 25: Current Project Portfolio
Development
Research
Commercial
Member
non-GMP
GMP
Instrument
BMS
Bayer
Baxter
Merck & Co
Amgen
Boehringer-Ingelheim
GSK
Drug Substance Release & Stability
Structure ID, Purification,
Lead Profiling
Method Screening
HPLC-UV/MS
HPLC-UV
Balance
HPLC-UV/MS
Structure ID
HPLC-MS
Fermentation
Process Control
Bioanalyzer
Small and Large Molecule CMC
Multiple types
Genentech
Elemental Impurities
ICP-MS
Assay, Purity
HPLC-UV
pH, Weighing, GC, Karl Fischer, TGA, NMR , Cell Density/Viability, Blood Gas Analyzer , Cell Culture Analyzer, Capillary Electrophoresis
…

## Slide 26: Amgen Project
LES
Instruments
Data Lake
(Hadoop)
ADF multiple techniques
(results only)
AF Taxonomies
pH
Weighing
HPLC
UV
MS
GC
Karl Fischer
TGA
NMR
Cell Density/Viability
Blood Gas Analyzer
Cell Culture Analyzer
Capillary Electrophoresis
…
APN Member PoCs
AF Taxonomies
ADF multiple techniques
(results only)
APN Member “ELN”
APN Member “SDMS”
GMP Development

## Slide 27: GSK Project
ELN
ADF
Balance
HPLC
APN Member PoCs
ADF
APN Member “CDS”
APN Member “ELN”
APN Member “ELN”
Allotrope Taxonomies
Stability Testing
Release Testing Methods
SOPs
GMP Development

## Slide 28
The Framework will provide Business benefit
Less Manual Document Preparation
Find data quickly/logically
Eliminate Copy/paste
Improved Data Integrity
Eliminate error due to manual text entry or transcription
Seamless data exchange & with partners & CROs
One data file format
One consistent vocabulary
No more Transcription/conversion
Source agnostic
Complete, consistent, accurate metadata
Reduced cost & complexity to CROs, CMOs, partnerships
Lower Data Management Costs
Interoperability
Facilitate Regulatory Compliance
Improved instrument & software validation tracking
Extracting Knowledge & Value from Data
Remove data silos
Facilitates data mining & analytics
Future-proof against future data migrations
Reduced technical debt: no more maintenance of legacy systems
Reduced complexity in system documentation
Greatly enhance speed to answer/decision
Create an ecosystem for innovation
Simpler to support questions/investigations
Improved archiving
What are your priorities?

## Slide 29
Thank you!